## Slide 1
MOS Capacitors
ECE 2204

## Slide 2
Some Classes of Field Effect Transistors
Metal-Oxide-Semiconductor Field Effect Transistor
  MOSFET, which will be the type that we will study in this course.
Metal-Semiconductor Field Effect Transistor
  MESFET, typically fabricated with III-V semiconductors
Junction Field Effect Transistor
  JFET, resilient to electrostatic discharge (ESD)
High Electron Mobility Transistor or Modulation Doped Field Effect Transistor
  HEMT or MODFET, typically fabricated with III-V semiconductors
Fast Reverse/Fast Recovery Epitaxial Diode
  FREDFET
DNA Field Effect Transistor
  The conduction path is through a strand of DNA

## Slide 3
Field Effect Transistors
A voltage is applied to the gate of the transistor, which produces an electric field within the semiconductor.
  Typically, the gate current is zero.
The conductivity (or resistivity) of the path between two contacts, the source and the drain, is altered by the voltage applied to the gate.
  Device is also known as a voltage controlled resistor.

## Slide 4
MOS Capacitor
The operation of a metal-oxide-semiconductor is used to explain the operation of the MOSFET.
  In a MOSFET, the channel in the semiconductor, the oxide, and the gate metalization forms a MOS capacitor.
    The structure looks like a parallel plate capacitor where one of the plates is the semiconductor and the other is the gate metalization. The insulator between the parallel plates is the oxide.
Semiconductor
Oxide

## Slide 5
MOS Capacitor
eox
tox
eOX = eox eo where eox is the relative dielectric constant of the oxide.
Notes: <number>

## Slide 6
Operation of a MOS Capacitor
In the following analysis, it is assumed that the channel in the semiconductor is lightly doped with acceptors (i.e., p type).
  There are three regions of operation
    Accumulation (in this case, VG < 0 V)
    Depletion (in this case, 0 V ≤ VG ≤ VTN)
    Inversion (in this case, VG ≥ VTN)

## Slide 7
Accumulation (VG < 0 V)
An electric field E is induced by the applied voltage VG.
  More holes are at the oxide-semiconductor interface than expected from the concentration of acceptors.
    Holes are attracted to interface by the negative gate voltage.
    Electrons are repelled towards the body contact.

## Slide 8
Depletion (0 V < VG ≤ VTN)
The induced electric field E causes the concentration of holes at the oxide-semiconductor interface to be smaller than the acceptor concentration and the electron concentration to be greater than expected.

## Slide 9
Depletion Mode Capacitance
The unscreened acceptors and a higher than expected electron concentration at the oxide semiconductor interface induce an electric field in the semiconductor, producing a depletion region to form.

## Slide 10
Inversion (VG ≥ VTN)
The gate voltage is large enough that the concentration of electrons at the oxide-semiconductor interface is greater than the concentration of holes.
  The type of the semiconductor has effectively been converted from p-type to n-type. The voltage when n = p at the oxide-semiconductor interface is called the threshold voltage, VTN.

## Slide 11
Inversion Mode Capacitance
A depletion region still exists in the semiconductor, but is now located between the inverted (n-type) region and the remaining p-type semiconductor.
  The thickness of the depletion region W is constant, even if VG increases so the magnitude of the MOS capacitance is constant.

## Slide 12
MOS Capacitance
Is largest in the accumulation mode when VG ≤ 0 V
Is smallest in the inversion mode when VG ≥ VTN
Varies with VG in the depletion mode

## Slide 13
Questions
If the acceptor concentration is increased, will be threshold voltage have to increase or decrease?
Do you expect the threshold voltage to increase or decrease as the temperature of the MOS capacitor is increased?
Can you explain how the electron and hole concentration varies with VG if the semiconductor is initially n-type instead of p-type?